## Slide 1: EnableIoT Workshop
Tuesday 22nd March

## Slide 2: Agenda
Downloads
  Download software for EnableIoT and Edison (for use later)
What is EnableIoT
  Getting started
  How data is stored
Pushing sensed data
  Setting up sensors on Intel Edison
  Registering the Edison and sensors with EnableIoT
  Pushing data with iotkit-agent
Requesting data

## Slide 3: Agenda
Downloads
  Download EnableIoT and Edison software (for use later)
What is EnableIoT
  Getting started
  How data is stored
Pushing sensed data
  Setting up sensors on Intel Edison
  Registering the Edison and sensors with EnableIoT
  Pushing data with iotkit-agent
Requesting data

## Slide 4: Downloads
Edison Getting Started
Choose operating system for download
In options, select to download everything
  Intel Edison drivers
  XDK – IDE
  …plus the rest

## Slide 5: Agenda
Downloads
  Download EnableIoT and Edison software (for use later)
What is EnableIoT
  Getting started
  How data is stored
Pushing sensed data
  Setting up sensors on Intel Edison
  Registering the Edison and sensors with EnableIoT
  Pushing data with iotkit-agent
Requesting data

## Slide 6: What is Enable IoT
What is EnableIoT
  Getting started
    Create user account
    Explore UI
  Github page
  How data is stored
    Accounts, devices and components

## Slide 7: Agenda
Downloads
  Download EnableIoT and Edison software (for use later)
What is EnableIoT
  Getting started
  How data is stored
Pushing sensed data
  Setting up sensors on Intel Edison
  Registering the Edison and sensors with EnableIoT
  Pushing data with iotkit-agent
Requesting data

## Slide 8: Pushing Sensed Data
Setting up sensors on Intel Edison
  Configuring the Intel Edison
  Adding sensors to Edison with Grove kit
  XDK and uploading code to read sensors
Registering the Edison and sensors with EnableIoT
Pushing data with iotkit-agent

## Slide 9: Pushing Sensed Data
Setting up sensors on Intel Edison
  Configuring the Intel Edison
    Plug in both USB cables
    Check the COM port for Edison
    ssh into Edison on COM port (using putty or equivalent) – Baud rate = 115200
    Press enter once
    Login: root
    configure_edison --wifi
      Select number of network to join
      Enter password
    configure_edison --password
      Enter a new password for Edison
Notes: Serial port name on Mac – ls /dev/tty.*
screen command for Mac - screen /dev/tty.[yourSerialPortName] [yourBaudRate]

## Slide 10: Pushing Sensed Data
Setting up sensors on Intel Edison
  Adding sensor to Edison with Grove kit
    Connect the Grove kit shield
    Connect a light sensor to A0

## Slide 11: Pushing Sensed Data
Setting up sensors on Intel Edison
  XDK and uploading code to read sensor
    Open XDK
    Create a new project ‘analog_read’ using the Analog Read template
    Connect to Edison - IoT Device
    Upload code to Edison
    Run code to see sensor reading
    Connect temperature sensor to A1
    Connect sound sensor to A3 **
    ** A2 sometimes gives problems

## Slide 12: Pushing Sensed Data
Registering the Edison and sensors with EnableIoT
  in terminal/cmd type
    ‘iotkit-admin test’ - to test connection to EnableIoT
    ‘iotkit-admin device-id’ - to see the ID of your Edison device
    ‘iotkit-admin set-device-id <your-device-id>’ - to change ID of your Edison device
  Activate your Edison device on EnableIoT
    Get activation code - Main menu > Account > Details (refresh activation code and view)
    ‘iotkit-admin activate <your-activation-code>’
  Check updates in EnableIoT
    Devices should list your Edison with correct device ID

## Slide 13: Pushing Sensed Data
Registering the Edison and sensors with EnableIoT
  EnableIoT Catalog and sensor registration
    Main menu > Account > Catalog
    Create new catalog items for ‘light’ and ‘sound’
  Register sensors on Edison with EnableIoT using Catalog types
    ‘iotkit-admin catalog’
    View catalog types - you should see light and sound also
    Make note of ‘measure’ and ‘id’ fields
    ‘iotkit-admin register <measure> <catalog id>’
    Do this for light, temp and sound
  Check updates in EnableIoT
    Main menu > Charts >

## Slide 14: Pushing Sensed Data
Registering the Edison and sensors with EnableIoT
  Send test reading to EnableIoT
    ‘iotkit-admin observation light 250’
    ‘iotkit-admin observation temperature 21’
    ‘iotkit-admin observation sound 345’
  Check EnableIoT for updates
    Main menu > Charts
  Start iotkit-agent running
    ‘systemctl start iotkit-agent’ **
    ‘systemctl status iotkit-agent’
    ** (systemctl stop iotkit-agent)
Notes: iotkit-agent: process running in Edison listening on port 41234

## Slide 15: Pushing Sensed Data
Pushing data with iotkit-agent
  in XDK create new project from blank template
  copy and paste code from:
    https://github.com/sarah-g/enable-workshop
  code captures sensor readings every 1 second and sends to port 41234
  Check EnableIoT for updates
    Main menu > Charts > select device and sensor types > select graph view
Notes: iotkit-agent: process running in Edison listening on port 41234

## Slide 16: Agenda
Downloads
  Download EnableIoT and Edison software (for use later)
What is EnableIoT
  Getting started
  How data is stored
Pushing sensed data
  Setting up sensors on Intel Edison
  Registering the Edison and sensors with EnableIoT
  Pushing data with iotkit-agent
Requesting data

## Slide 17: Requesting data
EnableIoT REST API

## Slide 18: Authorization Tokens
Device Token
Assigned to a device at the time activation.
Used to create time series and send observation
User Token
    Used for pulling data from Enable IoT. Derived from the user’s credentials. Enables access to the user resources on EnableIoT

## Slide 19: Authorization Header: Token must be sent using the HTTP authorization header. Example:
*REST requires authorization token
Authorization: Bearer<space><token>
Authorization: Bearer eyJ0eXAiOiJKV1QiLCJhbGciOiJSUzI1NiJ9....

## Slide 20: Submit Data
Param | Type | Description | Value
Authorization | HTTP Header | Device Token | Authorization: Bearer eyJ0eX...
Content-Type | HTTP Header | Type of body content | application/json
DeviceId | URL Slug | The ID of the device from which the data is being submitted | AA-BB-CC-DD-EE-FF-11

## Slide 21: Submit Data
{
"on": 1354741967799,
"accountId": "550e8400-e29b-41d4-a716-446655440000",
"data": [
{
"componentId": "436e7e74-6771-4898-9057-26932f5eb7e1_01",
"on": 1354741966688,
"loc": [ 45.5434085, -122.654422, 124.3 ],
"value": "26.7"
},{
"componentId": "436e7e74-6771-4898-9057-26932f5eb7e1_03",
"on": 1354741966677,
"value": "TWFuIGlzIGRpc3Rpbmd1aXNoZWQsIG5vdCBvbmx5IGJ5IGhpcyByZWFzb24sIlciBhbmltYWxzLCB3aGljaCBpcyBhIGx1c3Qgb2YdGhlIG1"
}
]
}

## Slide 22: Request Data
Param | Type | Description | Value
Authorization | HTTP Header | Access Token | Authorization: Bearer eyJ0eX...
Content-Type | HTTP Header | Type of body content | application/json
accountId | URL Slug | The ID of an Account | 534da46c820cb9f74a0d3de6

## Slide 23: Request Data
{
"from": <milliseconds from epoch>,
"to": <milliseconds from epoch>,
"targetFilter": {
"deviceList": [
"<ID>"
]
},
"metrics": [
{
"id": "<component_id>“
}
]
}

## Slide 24: Request Data
from | to | meaning
0 | missing | Return all data available
-86400 | missing | return all data with timestamps in the last 24 hours (86,400 seconds)
1407979291000 | 1407980711000 | return all observations with timestamps between 2014-08-13T18:21:31.000 UTC and 2014-08-13T18:45:11.000 UTC
*epoch : milliseconds from 1 January 1970

## Slide 25: Response:
{
"from": 1234567890,
"to": 1234567890,
"maxPoints": 100,
"series": [
{
{
"deviceId": "D2",
"deviceName": "D2",
"componentId": "76a95112-2159-4ee6-8e91-6a69b9c51edc",
"componentName": "Humidity 1",
"componentType": "humidity.v1.0",
"points": [
{"ts":9874569871,"value":"55"},
{"ts":9874569899,"value":"65"}
]
}
]
}

## Slide 26: Node JS

## Slide 27: Receiving Token
var get_token= function(username, password, MyCallBack){
var url = util.format("%s/auth/token",base_url);
var payload = {"username": username, "password": password};
var token;
make_request(make_options(url, "POST", payload),
function(err, data){
if (err) MyCallBack(err);
if (data) {
token = data.token; console.log("Token: " + token);
return MyCallBack(token);
}
});
};

## Slide 28: Getting Username
var get_user_id=function(token_t, MyCallBack){
var url = util.format("%s/auth/tokenInfo",base_url);
var user_id;
var payload={};
make_request(make_options(url, "GET", payload,token_t),
function(err, data){
if (err) MyCallBack(err);
if (data) {
user_id = data.payload.sub;
console.log("User Id: " + user_id);
return MyCallBack(user_id);
}
});
};

## Slide 29: Getting Account ID
var parse_account_id = function(obj,acn,MyCallBack){
var result = null;
Object.keys(obj).forEach(function(account_id) {
var account_args = obj[account_id];
Object.keys(account_args).forEach(function(arg) {
var arg_val = account_args[arg];
if (arg == "name" && arg_val == acn){
//console.log("2. Account Id:"+account_id);
result = account_id;
return MyCallBack(result);
}
});
});
};

## Slide 30: Pulling Observations
var get_observation=function(account_id, devic_id, component_id,period,token_t, MyCallBack){
var url = util.format("%s/accounts/%s/data/search",base_url,account_id);
//var dataset;
var search = {
"from": period,
"targetFilter": {
"deviceList": [g_device_id]
},
"metrics": [
{
"id": component_id
}
]
};

## Slide 31: Pulling Observations
make_request(make_options(url, "POST", search, token_t),
function(err, data){
if (err) MyCallBack(err);
if (data) {
return MyCallBack(JSON.stringify(data)); }
});
};

## Slide 32: Print Observation
var print_observation_counts = function(obj){
console.log("1: "+obj);
};

## Slide 33: Request
var make_request = function(options, callback){
request(options, function (error, response, body) {
if (!error && (response.statusCode === 200 ||
response.statusCode === 201 ||
response.statusCode === 204)) {
process_response(response, body, function(json_data) {
return callback(null, json_data);
});
} else {
error = error || body;
return callback(error);
}
});
};

## Slide 34: Response
var process_response = function(res, body, callback) {
var data = null;
if (res.statusCode === 200 || res.statusCode === 201) {
if (res.headers['content-type'] &&
res.headers['content-type'].indexOf('application/json') > -1) {
data = body;
} else {
data = null;
}
} else if (res.statusCode === 204) {
data = { status: "Done" };
}
return callback(data);
}

## Slide 35: Parameters for Request
var make_options = function(url, method, data, token){
var options = {
"url": url,
"proxy": null,
"method": method,
"json": true,
"followAllRedirects": true,
"strictSSL": false,
"body": data || {},
"headers": {}
}
if (process.env.PROXY) {
options.proxy = process.env.PROXY;
options.strictSSL = false;
}
if (token) options.headers = { "Authorization": "Bearer " + token };
return options;
}

## Slide 36
echo "src intel-iotdk http://iotdk.intel.com/repo/1.1/intelgalactic" > /etc/opkg/intel-iotdk.conf
vi /etc/opkg/base-feeds.conf
src/gz all http://repo.opkg.net/edison/repo/all src/gz edison http://repo.opkg.net/edison/repo/edison src/gz core2-32 http://repo.opkg.net/edison/repo/core2-32
opkg update opkg upgrade
opkg install python-pip ----------------------------------------------------
(pip install --upgrade pip)